## Slide 1
Lecture 6: Switching
Nick McKeown
CS244
Advanced Topics in Networking
Spring 2020
“High-speed switch scheduling for local-area networks”
[Tom Anderson, Susan Owicki, James Saxe, Chuck Thacker. 1993]

## Slide 2: Context
Tom Anderson
At the time: DEC SRC (Palo Alto)
Professor of CS, University of Washington
Previously: UC Berkeley, EECS
Susan Owicki
At the time: DEC SRC (Palo Alto)
Before that: Prof of EE & CS, Stanford
Today: Marriage and Family Therapist, Palo Alto
James B. Saxe
At the time: DEC SRC (Palo Alto)
After that: Compaq and HP Labs
?
Chuck Thacker (d. 2017)
At the time: DEC SRC (Palo Alto)
Before that: Xerox PARC (“Alto”)
After that: Microsoft
2010 Turing Award Winner
At the time the paper was written…
WWW was new, and Internet traffic was growing fast
Fastest Ethernet networks ran at 100Mb/s
Lots of interest in building faster switches and routers
Lively debate about an alternative to the Internet, called “ATM”

## Slide 3: But first…

## Slide 4: A few words about packet queues…
R = line rate.
e.g. 100M bit/s, 10Gb/s
Observation: With one arrival “line” at the same rate, the queue is always empty (or at most one store-and-forward packet). The arrival process is “bounded” by R.
Q: For any “load” what arrival pattern leads to the most customers in the queue?
Packet buffer
R
R
time
Cumulative arrivals, A(t)
R
gradient R
Cumulative bits
R
R
R
Q: For any “load” what arrival pattern leads to the most customers in the queue?
time
Cumulative arrivals, A(t)
R
gradient R
Cumulative bits
2R
q(t)
Observation: The arrival rate is “bounded” by R on average.

## Slide 5: Different cases for
time, s
0.5
1
1.5
2
1
line 1
line 2
Q: How big does the buffer need to be?
time, s
0.5
1
1.5
2
2
line 1
line 2
Q: How big does the buffer need to be?
time
1hr
2hr
3hr
4hr
3
line 1
line 2
Q: How big does the buffer need to be?
Observation: For a given arrival rate, in order to know the queueing delay, we need to know the pattern (or “process”) of arrivals.

## Slide 6: Background
2
3
4
1
N
…
…
…
A switch, or router, with N “ports”.
Each port runs at rate R b/s.
We say the “switching capacity” is N x R b/s.
R
R
R
R
R
1
R
R
R
R
R
R
2
3
N
…

## Slide 7: An output-queued (OQ) switch
R
R
1
R
R
R
R
R
R
2
3
N
…
Properties of an OQ switch
All buffering takes place at the output.
Output queues must be able to write packets at rate N x R.
Consequences
“Work conserving”: Whenever there is a packet in the system, its output is busy sending a packet. No unnecessary idling.
Average delay is minimized.
But memory bandwidth limits the switching capacity.

## Slide 8: Traffic Matrix
R
R
1
R
R
R
R
R
R
2
3
N
…
0.1
0.2
0.2
0.4
Traffic matrix,
is the fraction of traffic from input i to output j
0.1 0.2 0.2 0.4
0.2 0.3 0.1 0.1
1.0 0.0 0.0 0.0
0.1 0.4 0.3 0.1
For example:
Note that the row (input) sum:
Uniform Traffic Matrix:
1
Total traffic rate to each output is
Non-oversubscribed TM:
Notes: Note that 1st column of the example is “oversubscribed” to output 1.

## Slide 9: OQ Switches and “100% Throughput”
If we send traffic according to any non-over-subscribed traffic matrix to an OQ switch (with infinite buffers) then the output rates correspond to the column sums.
i.e. The traffic rate at output
Put another way, an OQ switch can “keep up” with any reasonable traffic matrix we throw at it.
We often say an OQ switch can “sustain 100% throughput”.
Q: What happens if the buffers are finite?

## Slide 10: An input-queued (IQ) switch
R
R
1
R
R
R
R
R
R
2
3
N
…
Properties of an IQ switch
All buffering takes place at the input.
Input queues only need to be able to write packets at rate R (instead of N x R).
Consequences
Can build a switch N times faster.
But, a packet can be held up by packet ahead destined to a different output.
Hence an IQ switch is not “work conserving”. It can unnecessarily idle.
May not achieve “100% throughput”.
Average delay is not minimized.

## Slide 11: Head of Line Blocking

## Slide 12: Head of Line Blocking
IQ switch with uniform traffic matrix,
Load,
Delay, d
1
0
0.5
3/2
0.75
5/2
Poisson arrivals:
OQ Switch
0.58
Poisson arrivals:
Observation: HOL Blocking means we lose
42% of the switching capacity
IQ Switch
Karol ‘87
Notes: Uniform is the most benign traffic pattern.
Poisson is the most benign arrival process.
Yet, HOL blocking limits IQ to only 58.6%

## Slide 13: What does the “58%” result mean?
R
R
1
R
R
R
R
R
R
2
3
N
…
R
R
Arrival rate
Departure rate
R
R
Arrival rate
Departure rate
OQ switch
R
R
Arrival rate
Departure rate
IQ switch uniform TM, Poisson

## Slide 14: Virtual Output Queues (VOQs)

## Slide 16: Basic idea
With a VOQ, a packet cannot be held up by a packet in front of it, destined to a different output.
Q: With VOQs, does/can 58% become 100% throughput?
R
R
Arrival rate
Departure rate
IQ switch uniform TM, Poisson
?
R
R
Arrival rate
Departure rate
IQ switch with VOQs
Any TM, Any arrivals

## Slide 17: 100% Throughput
Reminder: “100% throughput” is equivalent to
For a non over-subscribing traffic matrix, queues don’t grow without bound. i.e. for every queue in the system.
Observations:
  Burstiness of arrivals does not affect throughput
  For a uniform Traffic Matrix, solution is trivial!

## Slide 18: An input-queued (IQ) switch with VOQs and a crossbar
R
R
1
R
R
R
R
R
R
2
3
N
…
N2 VOQs
crossbar
…
R
R
R
R
1
2
3
N
R
1
R
R
R
2
3
N
…
Observation: scheduling is equivalent to choosing a permutation.

## Slide 19
N2 VOQs
crossbar
bipartite
request
graph
bipartite
match
e.g. “maximum size match”

## Slide 20: Crossbar schedule
crossbar
Fixed cycle of permutations:
crossbar
crossbar
crossbar
R
R
, therefore
arrival rate departure rate.
True for all VOQs, therefore
100% throughput for uniform TM
uniform TM
schedule

## Slide 21: 100% throughput for uniform traffic
Four (trivial) algorithms for a uniform traffic matrix:
Cycle through permutations in “round-robin” (i.e. previous slide).
Each time, randomly pick one of the permutations in (1).
Each time, pick a permutation uniformly and at random from all possible N! permutations.
Wait until all VOQs are non-empty, then pick any algorithm above.

## Slide 22: Quick recap so far

## Slide 23: An input-queued (IQ) switch
R
R
1
R
R
R
R
R
R
2
3
N
…
Properties of an IQ switch
All buffering takes place at the input.
Input queues only need to be able to write packets at rate R (instead of N x R).
Consequences
Can build a switch N times faster.
HOL Blocking: a packet can be held up by packet ahead destined to a different output.
Hence an IQ switch is not “work conserving”. It can unnecessarily idle.
May not achieve “100% throughput”.
Average delay is not minimized.

## Slide 24: Head of Line Blocking
IQ switch with uniform traffic matrix,
Load,
Delay, d
1
0
0.5
3/2
0.75
5/2
Poisson arrivals:
OQ Switch
0.58
Poisson arrivals:
Observation: HOL Blocking means we lose
42% of the switching capacity
IQ Switch
Karol ‘87
Notes: Uniform is the most benign traffic pattern.
Poisson is the most benign arrival process.
Yet, HOL blocking limits IQ to only 58.6%

## Slide 25: 100% throughput easy for uniform traffic
Four (trivial) algorithms for a uniform traffic matrix:
Cycle through permutations in “round-robin”.
Each time, randomly pick one of the permutations in (1).
Each time, pick a permutation uniformly and at random from all possible N! permutations.
Wait until all VOQs are non-empty, then pick any algorithm above.

## Slide 26: Q: So why did the authors need Parallel Iterative Matching (PIM)?
Because in practice, arrivals are not uniform.
(If know the matrix, we can still create a cycle of permutations to serve every VOQ at the rate in the traffic matrix).
In practice we don’t know the traffic matrix.
Hence, PIM….

## Slide 27: Parallel Iterative Matching A maximal bipartite match
1
2
3
4
1
2
3
4
Request
1
2
3
4
1
2
3
4
Grant
uar selection
1
2
3
4
1
2
3
4
1
2
3
4
1
2
3
4
Accept
uar selection
Iteration 1:
1
2
3
4
1
2
3
4
Iteration 2:
1
2
3
4
1
2
3
4
Q: Are we done?
Q: Is a larger match possible?

## Slide 28: PIM Properties
Inputs and outputs make decisions independently and in parallel.
Guaranteed to find a maximal match in at most N iterations.
Typically completes in much fewer than N iterations.
A maximal match is guaranteed to be at least half the cardinality (size) of a maximum match.
Q: How large is a maximal match compared to a maximum match?

## Slide 29: Parallel Iterative Matching
Simulation
16-port switch
Uniform traffic matrix
IQ + FIFO
VOQ + Maximum
Size Match
Output Queued
Note log scale

## Slide 30: Parallel Iterative Matching
PIM with one iteration
Simulation
16-port switch
Uniform traffic matrix
IQ + FIFO
VOQ + Maximum
Size Match
Output Queued

## Slide 31: Parallel Iterative Matching
PIM with one iteration
Simulation
16-port switch
Uniform traffic matrix
PIM with four iterations
IQ + FIFO
VOQ + Maximum Size Match
Output Queued

## Slide 32: How many PIM iterations should be run?

## Slide 33: Parallel Iterative Matching Number of iterations
Consider the n requests to output j
Requesting inputs receiving no other grants
Requesting inputs receiving other grants
k
n-k
j

## Slide 34: Known methods for non-uniform traffic
1. 100% throughput is now known to be theoretically possible with:
  IQ switch, with VOQs, and
  An arbiter to pick a permutation to maximize the total matching weight (e.g. weight is VOQ occupancy)
M, Walrand and Anantharam, 1996

## Slide 35
N2 VOQs
bipartite
request
graph
bipartite
match
“maximum WEIGHT match”
crossbar
1
2
3
1
3
Observation: give preference to longer VOQs
Leads to 100% throughput for any traffic matrix.
Choose matching
that maximizes

## Slide 36: Known methods for non-uniform traffic
2. It is practically possible with:
  IQ switch, VOQs, all running twice as fast (i.e. choose and transfer two cells per cell time)
  An arbiter running a maximal match (e.g. PIM)
Intuition: Because maximal match is at least half the size of a maximum match, running twice as fast compensates for it.
Dai and Prabhakar, 2000

## Slide 37: Known methods for non-uniform traffic
3. 2 switch stages with a fixed schedule of permutations!
C-S Chang, 2001

## Slide 38: A 2-stage Load-balancing switch
N2 VOQs
crossbar
…
R
R
R
R
1
2
3
N
R
1
R
R
R
2
3
N
…
Intuition: If uniform traffic is so easy, can I make
non-uniform traffic “sufficiently uniform”?
Fixed cycle of permutations
R
1
R
R
R
2
3
N
…
Fixed cycle of permutations

## Slide 39: A 2-stage Load-balancing switch
N2 VOQs
…
R
R
R
R
1
2
3
N
R
1
R
R
R
2
3
N
…
R/N
R/N
R/N
R/N
Deceptively simple but works for non-uniform traffic!
Q: Where is the switching taking place?
Q: Can packets be mis-sequenced?

## Slide 40: End.