## Slide 1
Lecture 9: SDN (2)
Network Virtualization
Nick McKeown
CS244
Advanced Topics in Networking
Spring 2020
“Network Virtualization in Multi-tenant Datacenters,”
[Teemu Koponen et al, 2014]

## Slide 2: Context
Teemu Koponen
  Early employee Nicira
  Sigcomm Rising Star Award, 2012
  More recently, co-founder at Styra
Teemu

## Slide 3: SDN: In the context of bigger networking industry changes

## Slide 4: Computer Industry
Specialized
Operating System
Specialized
Hardware
Specialized
Applications
App
App
App
App
App
App
App
App
App
App
App
Open Interface
Linux
Mac
OS
Windows
(OS)
or
or
Open Interface
Microprocessor

## Slide 5: Networking Industry
Specialized
Operating System
Specialized
Hardware
Specialized
Features
App
App
App
App
App
App
App
App
App
App
App
Open Interface
Open Interface
Control Plane 1
Control Plane 2
NOX
Beacon
ONIX
POX
ONOS
Flood light
Trema
ODL
Ryu
Switch Chips
“Software is eating the world (of networking)”

## Slide 6: Network Function Virtualization (NFV)
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Middlebox
Middlebox
Middlebox
Middlebox
Public Internet
Firewalls
Load-balancing
NAT
Boundary routers
Deep Packet Inspection
DDoS Mitigation

## Slide 7: Network Function Virtualization (NFV)
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Middlebox
Public Internet
VM
VM
VM
VM
VM
VM
Packet
Forwarding
Packet
Forwarding
Firewalls
Load-balancing
NAT
Boundary routers
Deep Packet Inspection
DDoS Mitigation

## Slide 8: With hindsight, Disaggregation, SDN and NFV were probably inevitable
Part of a bigger trend towards the owners and operators of networks taking control of how they manage their networks

## Slide 9: Inevitable because…
Rise of Linux.
Rise of baremetal servers and data centers.
SDN: Rise of merchant switching silicon.
NFV: Rise of computer virtualization.

## Slide 10: Today

## Slide 11: Most networking equipment is disaggregating
Intra- and inter-datacenter networks
ISP routers and switches
WiFi APs
Cellular basestations (4G, 5G…)
Optical and Metro Transport
Residential broadband access
Enterprise network equipment: switch, router, firewall

## Slide 12: Network Virtualization

## Slide 13: “Modularity based on abstraction is the way things are done!”
Barbara Liskov (MIT) Turing Award Lecture 2009
Notes: As Barbara Liskov said about computer science: “Modularity based on abstraction is the way things are done!” Abstractions are arguably the foundation upon which computers and entire data-centers are built.
I actually think the past ten years in networking has been all about creating new abstractions for network control planes.

## Slide 14: Abstractions in computer systems
Virtual memory: Abstract illusion of infinite, private physical memory
File system: Uniform illusion of read/write data store.
Virtual Machine: User application cannot tell if it is running on a physical or virtual machine.
…
Notes: The world of computing is built on a foundation of clever abstractions.
The abstraction of virtual memory means our applications don’t have to worry about managing physical memory locations and caches. Abstractions for file systems means our applications can open, update and close files without needing to know what hardware the file system uses, or where it is located. The abstraction of an operating system means our applications don’t have to worry about how processes are scheduled and peripherals are shared.

## Slide 15: What is “network virtualization”?
In this context: The abstraction (or illusion) of a physical network in which the user, application (and possibly the administrator too) cannot tell if the network is physical or virtual.
Q: If true, what would be the benefits?

## Slide 16
Will Robert Brand:
…does this kind of virtualization have any advantages in aggregate? That is, under NVP, are there positive or negative externalities to running diverse logical topologies in the same datacenter?
Notes: Advantages:
DC owner can move VMs around without changing addresses. Why would that matter?
Can connect back to home network using same addresses
Can potentially allow each tenant to have its own network features. One might want IPv4, another IPv6, another might want firewalls, load-balancing; yet another might use flat Ethernet.
Can connect back to same home network using same features and middleboxes.
Can potentially move to new data center or cloud, if they are compatible.

## Slide 17: Early attempts at network virtualization
Example: VPN
Q: To what extent is this virtualization?
Web browser
Public Internet
Corporate HQ
VPN Server
VPN Client
IP Datagram
Tunnel
Hdr
IP datagram
IP Datagram
Notes: Not a clean abstraction: Just abstracts forwarding, not control.

## Slide 18: Early attempts at network virtualization
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Control Plane 1 (“Network OS”)
CP 1a
Control
Program
Control
Program
Example: Slicing
Network Slicer (e.g. FlowVisor)
Control Plane 2 (“Network OS”)
Control Plane 3 (“Network OS”)
Control Plane 4 (“Network OS”)
CP 1b
CP 2a
CP 2b
CP 3a
CP 3b
CP 4a
CP 4b
Each controller can read and/or write flow rules for its assigned portion of “header space” and topology
Q: To what extent is this virtualization?
OpenFlow
OpenFlow
OpenFlow
OpenFlow
OpenFlow
Notes: Slices up the header space resources; can’t support arbitrary address space.

## Slide 19: Trends at the time of writing
Data centers and clouds F efficiency matters
VMs F a vSwitch inside every server
SDN F abstraction for control

## Slide 20: Virtual vSwitch in every server
VM
VM
VM
Packet
Forwarding
vSwitch
OS
NIC
Control Plane
(“Network OS”)
OpenFlow
Q: How might the vSwitch help?
Notes: Provides a software control point inside every server.
Background: OVS (Open vSwitch) was created at the time, to go with NVP, and upstreamed to Linux distributed.

## Slide 21: SDN and Network Virtualization
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Global Network Map
Control Plane (“Network OS”)
Network Virtualization
Abstract Network View
Control
Programs
Control
Programs
Control
Programs
Notes: Note virtualization goes above control plane in this case: Each control program sees an abstract model of the network to control.

## Slide 22: Another way to create a VPN
VM
VM
VM
Packet
Forwarding
vSwitch
OS
NIC
Public Internet
NIC
Tunnel
Hdr
IP datagram
IP Datagram
VM
VM
VM
Packet
Forwarding
vSwitch
OS
NIC
Control Plane
(“Network OS”)
OpenFlow
OpenFlow
“If destination is remote,
encapsulate in IPsec”
Observation 1: Control Plane tells vSwitch how to process packets into/out of tunnel

## Slide 23: In a virtualized cloud service provider
VM
VM
VM
Packet
Forwarding
vSwitch
VM
VM
VM
Packet
Forwarding
vSwitch
VM
VM
VM
Packet
Forwarding
vSwitch
VM
VM
Packet
Forwarding
vSwitch
192.5.0.0/24
192.5.0.2
192.5.0.1
171.64.74.155
171.64.74.157
171.64.74.158
171.64.74.156
192.5.1.0/24
192.5.1.1
192.5.1.2
128.30.2.109
128.30.2.110
128.30.2.200
Control Plane
OpenFlow
OpenFlow
VM
A mesh of tunnels between all physical servers.
vSwitch translates addresses into and out of tunnels.
Observation: Tenant workloads (VMs) are isolated from each other.
Observation: VMs can move without changing address.

## Slide 24
VM
VM
VM
Packet
Forwarding
vSwitch
VM
VM
VM
Packet
Forwarding
vSwitch
VM
VM
VM
Packet
Forwarding
vSwitch
VM
VM
Packet
Forwarding
vSwitch
PHY-0/24
PHY-0.2
PHY-0.1
V-1.155
V-1.157
V-1.158
V-1.156
VM
PHY-1/24
PHY-1.1
PHY-1.2
V-0.109
V-0.110
V-0.200
PHY-0.2
PHY-1.1
IP datagram
IP Data
V-0.110
V-0.109

## Slide 25
VM
VM
VM
Packet
Forwarding
vSwitch
VM
VM
VM
Packet
Forwarding
vSwitch
VM
VM
Packet
Forwarding
vSwitch
VM
VM
Packet
Forwarding
vSwitch
PHY-0/24
PHY-0.2
PHY-0.1
171.64.74.155
171.74.74.157
171.64.74.158
171.64.74.156
VM
PHY-1/24
PHY-1.1
PHY-1.2
VM
171.64.74.160
PHY-0.1
PHY-GW
IP datagram
IP Data
V-1.155
V-1.160
“VIP-DIP Gateway”
VM

## Slide 26: Adding a distributed, virtual firewall
VM
VM
VM
Packet
Forwarding
vSwitch
VM
VM
VM
Packet
Forwarding
vSwitch
VM
VM
VM
Packet
Forwarding
vSwitch
VM
VM
Packet
Forwarding
vSwitch
PHY-0/24
PHY-0.2
PHY-0.1
V-1.155
V-1.157
V-1.158
V-1.156
VM
PHY-1/24
PHY-1.1
PHY-1.2
V-0.109
V-0.110
V-0.200
PHY-0.1
PHY-1.1
IP Data
V-0.200
V-0.109
Firewall
L2 Table
IPv4 Table
IPv6 Table
ACL Table
Actions
Actions
Actions
Actions

## Slide 27: In general
VM
VM
VM
Packet
Forwarding
vSwitch
VM
VM
VM
Packet
Forwarding
vSwitch
VM
VM
VM
Packet
Forwarding
vSwitch
VM
VM
Packet
Forwarding
vSwitch
VM
OF0
OF1
OFn
Control Plane
OpenFlow
It is generically called: “Overlay network virtualization”
Q: To what extent is this “network virtualization” ?
Virtual middleboxes

## Slide 28: NVP is proactive: Pushes rules and state top-down
2: Datacenter owner configures
the networks: topologies and protocols.
1: Provide location,
state and topology.
Even as VMs move.
OVS control protocol.
3: Calculates forwarding pipeline model for each vSwitch and the state for each table. Pushes via OpenFlow and OVS control protocol.

## Slide 29: Top-down proactive control
Goals:
  Scale: Controller does not process packets
  Isolation: To continue if VMs, vSwitches fail F controller is a distributed, resilient cluster
Immense computational challenge!
NVP is built on ONIX, a distributed SDN controller (used by Google)
Each NVP/ONIX controller manages some slices (shards); and is responsible for others, if a controller fails.
NVP uses Apache Zookeeper for
  Leader election: to coordinate global resources and load-balancing) and
  Label allocation: Logical egress port must be globally unique

## Slide 30: Scaling Challenges
Margalit Ruth Glasgow:
Technical question: The authors mention in the "Lessons Learned" that using OpenFlow requires O(n^2) operations to tailor flows for each hypervisor, vs the standard complexity of O(n) for the logical controller. Where do those numbers come from? Does the O(n) come from each VM having O(1) connections at once, and the O(n^2) from each hypervisor needing to always have a connection with each other hypervisor?
A: Yes.
Q: What did the authors plan for the next version of NVP?

## Slide 31
Neil Perry
This came out in 2014 (NSDI '14). Have any "simpler" systems that achieve the same goals as this been put forward since? NVP seems very complicated and hard to implement (lots of room for mistakes).
Ryan Smith:
How can you implement a similar concept without using a centralized OpenFlow-like model to avoid the scaling penalty?

## Slide 32: End.