## Slide 1
Lecture 10: Buffer Sizing
Nick McKeown
CS244
Advanced Topics in Networking
Spring 2020
“Sizing Router Buffers” [Appenzeller, et al. 2004]

## Slide 2: Context
Guido Appenzeller
  At the time: CS PhD student
  Founded Big Switch Networks
  CTO at VMware for networking
  Sigcomm Test of Time Award, 2015
At the time of writing
  Challenging to build ISP routers with big buffers
  80% of world’s SRAMs used for router and switch buffers/counters
  ISP routers sold with ~90% profit margin

## Slide 3: Why should we care?
Background
No universal agreement on how big a router buffer should be
Or why.
Yet buffers are a major cause of variation in packet delay.
Big buffers require large, slow DRAM memories…
…which complicate the design of large routers.
It would be nice if we could use single chip switches and routers

## Slide 4: Simple model of FCFS router buffer
B
C
C
C
C
1
N
Q: Why does the router have a buffer (or queue)?
Q: What factors determine the buffer’s size?
Notes: Factors:
Long-term congestion. (a) TCP-like flows, (b) Incast
Short-term burstiness. (a) random fluctuations, (b) Burstiness of a flow.
Memory technology. SRAM, DRAM, on-chip, off-chip. Speed and size.

## Slide 5: Simple model of a router
B
1
N
1
N
C
C

## Slide 6: Simple Internet queueing model

## Slide 7: Early Internet Models
Leonard Kleinrock
Professor at UCLA
1963: 1st theoretical study of packet switching using queueing theory
1969: 1st message sent over Internet.
UCLA IMP (Interface Message Processor)

## Slide 8: Example model of single packet queue
Poisson Traffic, fixed size packets
M/D/1
Poisson arrivals, rate l
B
C
Observations:
Packet drop rate is small
Independent of C, RTT, number of flows, etc.
  Define: Load
  Then: drop rate
loss < 1%
Notes: Poisson arrivals means “memoryless process”, exponentially distributed interarrival times. Conditionally unioform. Most benign type of arrival.
Tantalizing result; remember for later. This model can be composed to create networks of switches that can be analyzed. (Kleinrock)

## Slide 9
Q: How well does this model fit today’s Internet?
The model assumes traffic is generated “open loop” by the source.
Today’s Internet carries mostly TCP traffic, which uses a closed loop congestion control algorithm.
Notes: TCP is closed loop. Flow behavior determined by congestion control loop.

## Slide 10: With multiple flows, RTT is less variable
A
B
Router buffer
Link rate = C
Link rate > C
Observations:
  An arriving packet sees a usually-full queue
  RTT is pretty much constant (very different from single flow case)
  Drops are random events

## Slide 11: One flow vs multiple flows
t
cwnd
Buffer occupancy and RTT
Buffer occupancy and RTT
t
(Zoom in)
cwnd
One of the flows
One flow
t
Buffer
Occupancy
and RTT
Multiple flows

## Slide 12: Geometric intuition for throughput equation
A3
A2
A1
Drop
t
cwnd
1
RTT
W1
W2
Area
But
Therefore, =
Expected Area,
Segments sent during
Throughput:
Throughput,
Drop rate,
Combining…
segments/sec
Combining
Note: To convert from packets/second to bits/second, multiply throughput by the packet size (e.g. MSS)
?
Notes: “width” of A is W/2, so area is (3/8)*W^2

## Slide 13: Interpreting the throughput equation
If RTT doubles, throughput halves.
If packet drop rate increases from 1% to 4%, throughput halves.
Notes: Long RTT flows are penalized: If we double the RTT we can expect the rate to halve! This is clearly not a good property and is often identified as a weakness of the AIMD approach.
Similarly, the rate is very sensitive to the
R1/R2 = sqrt( p2/p1 ). i.e. if p2 = 4%, p1 = 1%, then the rate is HALVED.

## Slide 14: One reason to care about buffer size
With on-chip buffers we can build
higher capacity switch ASICs

## Slide 15: Switch Chips are Limited by Serial I/O Capacity to the outside world
1
2
3
N
.
.
.
.
.
.
.
.
.
.
.
R
e.g. 12.8 Tb/s = 128 x 100Gb/s
Single chip switch ASIC
Small on-chip buffering
e.g. 64 Mbytes
1
2
3
N/2
.
.
.
.
R
Switch ASIC with external memory
Large off-chip buffering
e.g. 8 Gbytes
DRAM
Switch ASIC #1
I/O Capacity: C
Switch ASIC #2
I/O Capacity: C/2

## Slide 16: Switch Chips are Limited by Serial I/O Capacity
I/O Capacity: C
DRAM
I/O Capacity: C/2
C
C/2
DRAM

## Slide 17
C
How many switch chips with capacity C/2 do we need to make a router with capacity C?

## Slide 18: We need 6 ASICs with capacity C/2
I/O Capacity:C/2
C/4
DRAM
I/O Capacity: C/2
C/4
DRAM
I/O Capacity: C/2
C/4
DRAM
I/O Capacity: C/2
C/4
DRAM
I/O Capacity: C/2
DRAM
I/O Capacity: C/2
DRAM
Total Router Capacity:
C/8
C/8
C/8
C/8

## Slide 19: It is worth understanding where and when small on-chip buffers suffice

## Slide 20: A brief history of buffer size

## Slide 21
1988
2019
Congestion Avoidance
and Control
VJ & MK
1994
High Performance
TCP in ANSNET
CV & CS
A
B
C
B
“Buffer size should equal the bandwidth delay product”
Notes: In their landmark paper in 1988, Van Jacobson and Mike Karels described how AIMD and slow start had been added to TCP for congestion control, based on the AIMD proposal from Raj Jain’s technical report the year before.
In 1994, Curtis Villamizar and Cheng Song reported their work to make TCP work well in ANSNET, with and without RED. One of their conclusions is that you need a buffer size of 2T * C or the BDP to maintain 100% utilization of the bottleneck. This result became widely cited and became widely assumed to be correct. And many router manufacturers still quote this result to say that you need a BDP of buffering in a router.
This has the worrying effect of doubling the RTT if the bottleneck is congested; and even more so if all the routers along the path have a full BDP of buffer and are congested.
Before we get stuck into the details, and try to understand how big the buffer should be in different situations, I thought it would be useful to revisit where this result comes from. Why is it widely assumed we need a BDP of buffering in a router?
As I will explain, it’s a somewhat arbitrary artifact of the decision to divide the window size by 2 upon a packet loss. Let’s see why….

## Slide 22
A
B
C
B
2T
cwnd
time
cwnd
time
t
Notes: In the top right we have a simple network with one bottleneck link, carrying a single TCP flow.
Let’s see what buffer size we need, in order to keep the bottleneck link busy 100% of the time.
The graph shows a single sawtooth of the congestion window, varying from its max W-hat and halving each time a packet is dropped.

## Slide 23
cwnd
time
A
B
C
B
2T
cwnd
time
1
1
1
1
1
1
t
2
1
1
2
Notes: At the bottom of the sawtooth, the buffer just hits empty and, round trip time is at its minimum, which we call 2T. Each time a full window of packets is acknowledged, the window is incremented by one. Each time, the RTT also increases by one packet, because the queue always has one more packet in it. Until we reach the maximum window size. At this point, the buffer is full and the RTT equals 2T + B/C, the time for a packet to go through the buffer B/C plus the min RTT.
Notice that the link is full all the time all along the sawtooth from the bottom to the top, so we know the throughput is C all the time and the bottleneck link never goes idle.
In the next RTT a packet is dropped and TCP halves cwnd. At this point, the buffer drains and the RTT is back to the minimum RTT again. But the bottleneck link never goes empty.
By equating the capacity at (1) and (2) we easily conclude that B = 2T * C or the BDP.

## Slide 24: Time Evolution of a Single TCP Flow
A
B
C
B
2T
Notes: This is what we see if we simulate, emulate or measure the time evolution of a single TCP flow. These graphs are from Mininet.
On the left, we have exactly 1 BDP of buffering. The Buffer occupancy.- the red line in the middle – exactly tracks the Congestion Window. And so the ratio of the two, which is the utilization of the bottleneck link stays contant all the time.
If we make the buffer smaller than the BDP, the buffer goes empty once per sawtooth. And hence W/RTT can fall below C and the bottleneck link goes unnecessarily idle.

## Slide 25: Single TCP New Reno flow: 100% Throughput
If then
If then
If then i.e. if end host knows 2T, buffer size is independent of RTT
Example:
Example:
Example:
Example:
Notes: Notice that the buffer size equation is a direct consequence of how TCP works. In particular, because the window sized is halved each time there is a drop.
In the standard case, where cwnd is halved, it can lead to large buffers for a single flow. For example, if the minimum RTT is 100ms, a 10Gb/s link needs a 1Gbit (or 125Mbyte) buffer right before it.
It’s worth asking how big the buffer would need to be if TCPdivided cwnd by a different factor, instead of two.
It’s easy to deduce that if TCP divided cwnd by k on a drop, then we need this sized buffer. For example, if TCP divided cwnd by 1.5 instead of 2, the buffer size can be halved, while still maintaining 100% utilization of the bottleneck link.
The original Raj Jain paper had proposed dividing by 1.14, which means the buffer could be reduced by another factor of 3 to just 140Mbits, or less than 20Mbytes.
Finally, it’s worth wondering why the buffer size has a factor of RTT in it at all. Why does the buffer size depend on RTT? If the end host measures and knows the min RTT, it can pick k = 1 + a/minRTT, which means the buffer size now only depends on C. For example, if we pick a = 0.01, then the buffer size could be reduced to 50Mbits or about 6 Mbytes.

## Slide 26
1988
1994
2004
2020
Congestion Avoidance
and Control
VJ & MK
High Performance
TCP in ANSNET
CV & CS
Sizing Router
Buffers
GA, IK, NM
A
B
C
B
where N is the number of long-lived flows
Notes: The last results hold for a single flow. But real networks carry lots of flows, particularly big backbone networks and data-center networks.
When Guido Appenzeller was doing his PhD in 2004 we were wondering how big a buffer we need if a network is carrying lots of TCP flows. This led to the result that if the TCP flows are long-lived and not synchronized with each other, the buffer size can be reduced by the square root of N, where N is the number of long-lived flows.

## Slide 27: Synchronized Flows
Aggregate window has same dynamics
Therefore buffer occupancy has same dynamics
Rule-of-thumb still holds.
t

## Slide 28: Many TCP Flows
Probability
Distribution
B
0
~ Buffer Size
Notes: The rule of thumb for buffer sizing is based on a single TCP flow.
In the core of the Internet we have thousands of flows going though each link.
The buffer size we need here is inversely proportional to the variance of sum of these flows.
Since these flows are independent of each other, their sum has a Gaussian distribution, and the variance is decreased by the number of flows.

## Slide 29: Many AIMD flows: 100% Throughput
Example:
Example:
Q: Do you think will hold for other
congestion control algorithms…?
Notes: For example, with our example from before, if the same network carried 10,000 flows, the buffer requirements drops by a factor of 100, from 1Gbit to 10Mbits.
The graph plots the measured buffer size as a function of N, showing it follows the 1/ sqrt(N) curve quite closely.
We would love to know if this concentrating effect holds for other congestion control schemes, such as Vegas, DCTCP, BBR and others?

## Slide 30: You said
Nikhil Athreya
I think the assumptions made in the original paper are beginning to change. While they acknowledge that their work is mostly based off of TCP, they argue that single-packet sources (e.g. DNS) and constant-rate UDP sources (e.g. online games) can be modeled with short flows. However, a quick Google search tells me that (https://www.caida.org/research/traffic-analysis/tcpudpratio/) that the amount of UDP flows either has surpassed TCP flows or is at least comparable to it. I’m unsure how this would affect the results in this paper; perhaps because the results for short flows shows that average queue length is only dependent on link load and flow length, this shouldn’t be a problem, but I’d be interested to hear more about it.

## Slide 31: You said
Kevin Baichoo
It seems like from the backbone router vendor’s will disavow this smaller buffer sizes, as otherwise they can’t justify the prices for their equipment.
Esther Goldstein
Do buffer sizes today go by the rule-of-thumb equation, or has the equation been refined in a different way than what was proposed in the paper?
Isabel Victoria Papadimitriou
It seems that this is working under an assumption that TCP is TCP, and router manufacturers have to deal with that regarding buffer size. Why isn’t it the other way around (“this is the buffer size, make congestion control work”), or is it possible to think about some sort of joint optimization of buffer size and paradigm?

## Slide 32
1988
1994
2020
Congestion Avoidance
and Control
VJ & MK
High Performance
TCP in ANSNET
CV & CS
2004
Sizing Router
Buffers
GA, IK, NM
A
B
C
B
2006
Routers with
Very Small Buffers
ME, YG, AG, NM, TR
1. Paced Traffic
2. Link utilization < 80%
Assumptions
Only 20-50 packet buffers.
Consequences

## Slide 33
1988
1994
2020
Congestion Avoidance
and Control
VJ & MK
High Performance
TCP in ANSNET
CV & CS
2004
Sizing Router
Buffers
GA, IK, NM
A
B
C
B
2006
Routers with
Very Small Buffers
ME, YG, AG, NM, TR
2008
Experimental Study of
Router Buffers
NB, YG, MG, NM, GS

## Slide 34: Buffer Sizing Experiments
Small Buffers
  Stanford University dorm network
  University of Wisconsin
  Internet2
  Level 3 Communications
Tiny Buffers
  Internet2
  Sprint Advanced Technology Lab
  University of Toronto

## Slide 35: Level 3 Communications Experiments
High link utilization
Long duration (about two weeks)
Buffer sizes 190ms (250K packets), 10ms (10K packets), 2.5ms (2500 packets), 1ms (1000 packets)
Load balancing over 3 links (2.5 Gb/s each)

## Slide 36: Drop vs. Load, Buffer = 190ms, 10ms
Max Util = 96%

## Slide 37: Drop vs. Load, Buffer = 1ms

## Slide 38: Internet2 Experiments
Neda Beheshti
2010

## Slide 39: Summary of throughput and buffer size
Throughput
100%
Buffer Size
~ 90%
50-100 pkts

## Slide 40: End.